## Slide 1
ISAForge
ISAForge / ECE 4803 1
AI-guided RISC-V program optimization
Can learned selection find better feasible designs
with fewer hardware evaluations?
Real workloads → measured outcomes → intelligent selection
Midterm progress • ECE 4803 • October 28, 2026
Notes: SLIDE 1 — 25 seconds
SPOKEN SCRIPT
ISAForge asks whether learned predictions and an AI selection agent can find better RISC-V custom instructions with fewer expensive evaluations. We optimize verified whole-program performance under hardware constraints. Our contribution is the connection from real programs to measured labels to budgeted selection. Today we have a working pipeline, measured data, and preliminary comparisons—not yet a consistent machine-learning win.
SOURCES / Q&A (not part of timed script)
Scope: README.md; docs/research-foundation.md. Guarded AI-track results are separate from other hardware contexts in the team report.

## Slide 2
Research foundations
ISAForge / ECE 4803 2
Atasu et al. • DAC 2003
Legal dataflow candidates
Input/output limits and convexity
CIDRE • ICCAD 2025
Architecture-aware evaluation
Account for processor latency and timing
AutoTVM • NeurIPS 2018
Learn from measured performance
Pairwise ranking of alternatives
Gardner et al. • ICML 2014
Constrained Bayesian optimization
Balance benefit, feasibility, and measurement
Our test: measurement-efficient selection, validated on real processor outcomes.
Notes: SLIDE 2 — 30 seconds
SPOKEN SCRIPT
We build on established methods rather than inventing another enumerator. Atasu provides the dataflow and architectural constraints for legal instruction candidates. CIDRE emphasizes that benefits depend on the processor and its timing. AutoTVM motivates ranking alternatives using measured performance. Constrained Bayesian optimization motivates measuring promising candidates while accounting for feasibility. ISAForge tests this combination on whole-program PicoRV32 outcomes; we do not claim to reproduce these complete systems.
SOURCES / Q&A (not part of timed script)
Atasu, Pozzi & Ienne. Automatic Application-Specific Instruction-Set Extensions Under Microarchitectural Constraints. DAC 2003, 256–261. DOI 10.1145/775832.775897; methods §§4–7.
Rezunov et al. Automatic Microarchitecture-Aware Custom Instruction Design for RISC-V Processors. ICCAD 2025. DOI 10.1109/ICCAD66269.2025.11240781; arxiv.org/html/2509.15782v2, §§II–IV.
Chen et al. Learning to Optimize Tensor Programs. NeurIPS 2018. arxiv.org/pdf/1805.08166v4, §§3–4, Algorithm 1.
Gardner et al. Bayesian Optimization with Inequality Constraints. ICML 2014, PMLR32(2):937–945. https://proceedings.mlr.press/v32/gardner14.pdf, §§3.1–3.2.
Repository method reviews: docs/research-foundation.md; docs/selection-methods-review.md.

## Slide 3
Timeline and team contributions
ISAForge / ECE 4803 3
OCT 13–18
Traces + synthesis
early cost models
OCT 19
CRC32 + aha
processor pipeline
OCT 20–26
More workloads
+ selection tests
OCT 27
122-label scorecard
+ agent pilot
Contributor / evidence | Primary contribution area
Jason • Git evidence | ML, budgeted selection, agent tools, analysis
Yuuto • Git evidence | Hardware, selection engine, measurement tests
Sooraj • report attribution | Compiler, tracing, extraction and toolchain
Two project chats: ~46 h recorded turn time • roles need confirmation
Notes: SLIDE 3 — 20 seconds
SPOKEN SCRIPT
We started by collecting real benchmark traces and synthesizing isolated circuits for a hardware-cost model. Next we connected candidates to whole-program execution on PicoRV32, expanded the dataset, and tested selection policies. Two project chats record about forty-six hours of turn duration, including waits and interruptions, not training time. Team roles are provisional and need confirmation.
SOURCES / Q&A (not part of timed script)
Dated results directories October19–27; git history; docs/original-project-proposal.txt; supplied AgenticRiscPredictor.pdf. Codex history snapshot: two project chats record 15.82 and 29.97 hours of ended turn duration, approximately 45.8 hours combined, including tool waits and interruptions. The earlier 15.82 hours includes 4.51 hours across two interrupted turns. 72 distinct directly spawned subagent threads; activity is not training time or a research outcome. See codex-history-and-baseline.md. Team must confirm roles and aliases; Git alone cannot measure contribution shares.

## Slide 4
From workload to verified improvement
ISAForge / ECE 4803 4
1 Discover
Compile + trace
legal dataflow
2 Implement
Lower custom opcode
PicoRV32 PCPI
3 Verify
Program output
+ cycle count
4 Measure
Integrated LUT4
+ routed Fmax
candidates.py
workload_experiment.py
Verilator
Yosys + nextpnr
CRC32 reference: 32.39M cycles → 30.82M cycles = 1.051×
Unmodified program/core → compare cycles → verify area and timing
Restricted RV32 integer support • RTL simulation + FPGA synthesis/routing
Notes: SLIDE 4 — 35 seconds
SPOKEN SCRIPT
We wrote scripts that compile and profile workloads, extract legal candidates, and lower them to custom instructions. The evaluator executes each modified program with Verilator and checks correctness; Yosys and nextpnr measure integrated area and timing. The unmodified CRC32 reference took 32.39 million simulated cycles. The best candidate took 30.82 million, a 1.051 times common-clock speedup. These are simulation and FPGA tool results, not physical-chip stopwatch measurements.
SOURCES / Q&A (not part of timed script)
src/candidates.py extracts legal candidates; isaforge/workload_experiment.py orchestrates workload preparation and collection; isaforge/codesign.py implements ProcessorEvaluator; Verilator simulates, Yosys synthesizes, nextpnr routes. docs/codesign-loop.md; results/2026-10-19-codesign/independent-audit.json. Embench CRC32,170 benchmark repetitions; startup, independent checksum, warm-up and serial reporting excluded from counter window. Same RV32I PicoRV32, 8KiB RAM and 12MHz target. Baseline 32,387,382 cycles,1653 LUT4; index_offset 30,820,662 cycles,1684 LUT4 (+31), 1.050833x. Both correctness checked; same-clock speedup, not measured board runtime. Baseline synth/routing Fmax 68.49–77.16 MHz. Distinguish this unmodified reference from heuristic selection baselines.

## Slide 5
Dataset: measured programs, not synthetic labels
ISAForge / ECE 4803 5
Chart: Measured candidate/program pairs
| Embench | BEEBS | TACLeBench
Successful labels | 39 | 48 | 35
122 successful labels
14 workload groups
15 build/input contexts
4 failures retained
Earlier cost study: 713 formulas
Separate isolated-LUT labels
Train on other workloads; test on the entire held-out workload.
Notes: SLIDE 5 — 40 seconds
SPOKEN SCRIPT
Our first hardware-cost study grew from 301 to 713 distinct synthesized formulas across benchmark collections. Those isolated LUT labels are separate from the current whole-program dataset: 122 candidate-program measurements across fourteen workload groups, plus four charged failures. The chart shows its three benchmark suites. We hold out entire workloads. Our thirteen-policy screen includes 2,925 replays of existing measurements, not new hardware runs.
SOURCES / Q&A (not part of timed script)
Earlier area study: initial 301 formulas, later three collections 1,098 program/formula rows and 713 distinct formulas from 17 candidate-bearing programs; isolated LUT4 labels, not processor cycles. The frozen original-301 model evaluated 331 novel final formulas: structural linear 23.154 LUT4 MAE versus original XGBoost 87.595. Later all-713 deployment refit lacks a fresh independent test. See results/2026-10-13-prospective/README.md and docs/methodology-history.md. Current dataset: submissions/midterm-2026-10-28/dataset/; results/2026-10-27-final-selection-scorecard/scorecard.json. 15 build/input contexts;12 complete measured-pool oracles,2 censored. Embench39 labels/6 groups; BEEBS48/5; TACLeBench35/3. Original teammate hardware-branch data uses a distinct context and is not silently merged.

## Slide 6
The ML model: shallow boosted-tree ranking
ISAForge / ECE 4803 6
35 input features
Profile opportunity
Structure + operations
80 shallow trees
Depth 2
Learning rate 0.05
Ranking score
Relative ordering
Not a probability
Choose queries
Measure promising
candidates first
Training signal: measured speedup(A) > measured speedup(B)
Pairwise objective → encourage score(A) > score(B)
13 policies tested • 8 learned • 2,925 retrospective replays
Notes: SLIDE 6 — 40 seconds
SPOKEN SCRIPT
Our main challenger is XGBoost pairwise ranking, not a neural network. Thirty-five premeasurement features describe each candidate. We use measured speedup to order pairs within a workload, then fit eighty shallow trees. The output is a relative ranking, not a speedup or confidence probability. We tried eight learned policies in the final screen and five controls. Separate experiments tested Gaussian-process active learning. We assess selection quality, not just prediction error.
SOURCES / Q&A (not part of timed script)
isaforge/ranking.py: XGBRanker rank:pairwise;80 estimators,max_depth2,learning_rate0.05,min_child_weight1,reg_lambda1,subsample1,colsample_bytree1,hist,n_jobs1. isaforge/features.py:35 features. Relevance preserves ties within context. Measured target outcomes excluded from input features.

## Slide 7
Explainability and uncertainty
ISAForge / ECE 4803 7
Chart: Normalized contribution (%)
| Savings % | Locations | Size | Frequency | Other
Attribution share | 47.1035 | 11.1 | 7.2663 | 5.4586 | 29.0716
A high rank can still fail
Bitcount: top-ranked
1.0088× cycle speedup
+65 LUT4 > +64 cap
Correctness passed;
area made it infeasible.
Uncertainty guides questions; measured correctness and feasibility decide.
Notes: SLIDE 7 — 40 seconds
SPOKEN SCRIPT
Tree contributions show what drives the ranking: estimated instruction savings alone accounts for about forty-seven percent of normalized attribution. This describes the model’s behavior; it is not a causal explanation. A useful failure case is bitcount’s top-ranked candidate: it passes correctness and speeds up execution, but adds sixty-five LUT4 cells, exceeding the cap by one. Uncertainty should help us choose what to measure next. Ensemble disagreement and Gaussian-process estimates are available, but they are not yet calibrated confidence, and the ranker itself does not provide a confidence interval.
SOURCES / Q&A (not part of timed script)
results/2026-10-27-ranker-explainability/explanation.json; global_feature_contributions.csv. Normalized absolute additive tree contributions macro-averaged over14 held-out workloads; profile opportunity features account for66.39%. Local add(in0,andi(in1,15)) rank1/12;1.008782x,+65LUT4,61.82MHz. Uncertainty calibration remains unproved.

## Slide 8
AI agent architecture: implemented and planned
ISAForge / ECE 4803 8
WORKING CORE
Analyze + predict
Legal candidates
XGBoost rankings
LLM decision
Structured outputs
Function calling
Host + tools
Budget guardrails
Measure / finalize
Agent memory
Cycles, area, timing
Persistent ledger
Paid observations feed the next decision
PLANNED DECISION LAYER
Context window + token budget
Small LLM → escalate → strong LLM
OPTIONAL KNOWLEDGE LAYER
Approved history → chunk + embed
Hybrid search → rerank → RAG context
Both feed the LLM decision. Hidden target outcomes stay excluded.
LLMOps plan: version → evaluate → monitor → deploy
Track feasible speedup, evaluation cost, tool errors, tokens and latency.
Notes: SLIDE 8 — 45 seconds
SPOKEN SCRIPT
Our agent has four stages: analyze candidates and query ML predictions, choose a structured action, execute it through host guardrails, and record measured evidence. Paid observations feed the next decision. The lower half shows planned extensions. A bounded context builder would route routine decisions to a smaller language model and escalate difficult cases to a stronger one. Optional retrieval could supply approved historical evidence using chunking, embeddings, hybrid search and reranking. These components are not implemented yet. Across the system, LLMOps would version releases and track quality, tokens, latency and cost. We will judge every addition by verified feasible performance under the same measurement budget.
SOURCES / Q&A (not part of timed script)
Implemented: isaforge/bounded_selector.py, isaforge/selection_provider.py, scripts/run_codex_chat_selector.py; four tools list_candidates, predict, measure, finalize. Remote provider records model, tool calls, usage and latency where returned; active chat does not expose exact deployment ID or model-only usage. EDN consumed replay; Ascon three native measurements and live GP update defect fixed afterward. Proposed: smaller/stronger model routing, context/token budgets, retrieval, and complete cost/quality evaluation. No dynamic LLM routing, RAG/vector database, MCP integration, LangGraph, Ragas or production observability is claimed. See agent-architecture-plan.md.

## Slide 9
Baselines and a fair measurement budget
ISAForge / ECE 4803 9
Required comparisons
Frequency
Merit: operations saved × executions
Latency / cost-aware heuristics
Random + non-agent active learning
XGBoost + bounded LLM agent
Same rules for every policy
1 / 2 / 3 charged attempts
Added area ≤ 64 LUT4
Routed timing ≥ 12 MHz
Correctness must pass
Unqueried outcomes remain hidden
Endpoint: best VERIFIED, FEASIBLE performance found per evaluation budget.
Notes: SLIDE 9 — 35 seconds
SPOKEN SCRIPT
The unmodified program gives the performance reference. A different kind of baseline is a selection policy: frequency counts occurrences, while merit estimates operations eliminated times executions. We compare these with latency-aware heuristics, random search, and learned policies. Every method gets the same pool and one, two, or three charged attempts; unqueried results remain hidden. The measured oracle knows all outcomes and gives a retrospective ceiling, not a deployable policy. Historical training cost is tracked separately.
SOURCES / Q&A (not part of timed script)
Protocol: docs/research-foundation.md; scorecard.json. Simple merit uses projected instruction savings; do not label it a CIDRE reproduction. Primary endpoint best verified feasible cycle reduction; regret only for complete pools. Track target evaluations and elapsed time, historical training cost, fit/inference and agent costs separately. Exact isolated ranker fit/inference timing remains incomplete.

## Slide 10
Results: early gains, no consistent ML win
ISAForge / ECE 4803 10
Chart: Mean oracle regret (%) ↓
| 1 attempt | 2 attempts | 3 attempts
Merit | 1.132 | 0.465 | 0.015
XGB ranker | 0.842 | 0.439 | 0.07
Paired advantage of XGB
1 attempt: +0.290 pp
95% CI [−0.065, +0.849]
2 attempts: +0.027 pp
95% CI [−0.097, +0.177]
Merit is better at 3.
Early intervals include zero.
12 complete workload pools • retrospective comparison • merit remains fallback
Notes: SLIDE 10 — 75 seconds
SPOKEN SCRIPT
Here is the main selection result. The vertical axis is mean cycle-reduction regret relative to the best measured feasible candidate in each complete pool; lower is better. At one attempt, merit has 1.132 percent regret and the ranker has 0.842 percent. At two attempts they are almost tied. At three attempts, merit is better. The paired workload confidence intervals include zero for the early-budget advantages, so we cannot claim consistent superiority. Twelve workload groups have complete pool oracles; two incomplete groups are excluded from this regret calculation. The 2,925 policy-budget replays are dependent analyses of the existing measurements, not new hardware experiments. There is also an important diagnosis: all 122 historical cycle-speedup labels match the independently calibrated processor-latency calculation. This dataset therefore does not demonstrate a residual speedup relationship requiring machine learning. Our remaining challenge is learning which useful designs will be hardware-feasible and worth measuring. A previous three-source blind campaign favored both GP policies over merit at three attempts, but a later bitcount test favored the latency-cost heuristic. Those mixed results do not establish a general advantage. The Ascon pilot has no matched controls.
SOURCES / Q&A (not part of timed script)
results/2026-10-27-final-selection-scorecard/scorecard.json. Paired difference = merit regret minus ranker regret (percentage points): B1 +0.290 [−0.065,+0.849]; B2 +0.027 [−0.097,+0.177]; B3 −0.056 [−0.167,0.000]. Workload bootstrap;12 complete pools.14-group cycle-reduction means merit1.086/1.657/2.043%;ranker1.334/1.680/1.996%. Earlier frozen three-source campaign: GP 1.602185% mean cycle reduction vs merit 1.144539% at B3; only three sources and cooperative replay, no total-cost win established. Later bitcount B3 latency-cost heuristic found 0.174118% improvement while both GP policies returned baseline. docs/blind-source-campaign.md; results/2026-10-22-bitcount-report/results.md. Timing floor weakly tested:minimum selected feasible Fmax59.13MHz vs12MHz. Target mean eval time merit55.67/114.24/169.76s;ranker56.29/115.69/171.46s. No total-cost advantage established.

## Slide 11
Next milestone: an independent selection test
ISAForge / ECE 4803 11
Working now
Real workload → executable candidate
Measured cycles, area and timing
Whole-workload ML evaluation
Explainability + bounded agent tools
Next, in order
1 Freeze policies; test untouched workloads
2 Compare agent vs non-agent fairly
3 Validate uncertainty and total cost
4 Measure 1–3 instructions jointly
Success = better verified feasible performance per evaluation—not more models.
Notes: SLIDE 11 — 35 seconds
SPOKEN SCRIPT
We now have an end-to-end research system: real workloads, executable custom instructions, measured outcomes, learned ranking, and bounded agent tools. The next step is to freeze the policies before observing new workload results, then compare the agent and non-agent methods under identical budgets. We need better workload diversity and validated uncertainty before adding model complexity. Finally, we must implement and measure the selected one-to-three-instruction combination together. Individual speedups cannot be added. A reproducible heuristic win is still a useful scientific result.
SOURCES / Q&A (not part of timed script)
docs/HANDOFF.md; docs/ACTIVE_GOAL.md. Research paused at presentation checkpoint; no new collection implied by this deck. Next experiments require frozen controllers/policies, legal lowering and blind measurement contracts. Keep the original CRC32 and aha-mont64 experiments and all negative outcomes. No RTL-rewriting optimization agent.